## Slide 1: Individual Technical Presentation: Magnetic Resonance
Caleb Rozenboom

## Slide 2: Introduction
MRI changed the medical industry
Technology advanced in quantum physics, super conductors, and computer science

## Slide 3: History of the MRI
Harmful X-rays
  Absorption of x-ray beams
Low-resolution ultrasound
  Sound waves bounce off densities
Flat 2d
MRI better imaging and contrast with less risk
Takes longer and expensive

## Slide 4: History of the MRI
Developed by Isidor Isaac Rabi (1898-1988) [1]
Worked with Bohr, Pauli, Heisenberg
Discovered magnetic resonance
Nobel Prize in 1944
First images in 1970
First human subject in 1977
After being imaged he said, “It was eerie. I saw myself in that machine, I never thought my work would come to this.”

## Slide 5: Hydrogen Atom
Hydrogen atoms in body
Bar magnets
Evenly distributed probability
Net magnetization vector
Parallel and anti-parallel

## Slide 6: Nucluear Spin
Precession
Larmor Equation
ω is the Larmor frequency (MHz)
γ is the gyromagnetic ratio (in MHz/T)
  Specific to element
B is the magnetic field strength (T)

## Slide 7: Radiofrequency Pulse
RF (B1 in right picture)
Changes longitudinal magnetization vector (LMV)
Temporarily aligns in phase
Angle depends on intensity
Sends radiofrequency back

## Slide 8: Relaxation
Sends 90 degree RF
  Transverse Magnetization Vector
Free induction decay
T1 time:
  63% of LMV has been recovered [2]
T2 time:
  63% of TMV has been lost [2]
T1 and T2 are unique to different tissues
  T1 fat and T2 water

## Slide 9: Free Induction Decay Caveats
Applies to 90 degree only
Signal decays rapidly
  Requires fast scanner
T2* constant dephasing
  Not actually uniform
  Experience B field differently
  Signal dropout
How to fix? 180 RF correction pulse
More energy: echo
Done over and over until no more energy

## Slide 10: Spin Echo Sequence

## Slide 11: References
[1] July, 1977: MRI Uses Fundamental Physics for Clinical Diagnosis https://www.aps.org/publications/apsnews/200607/history.cfm#:~:text=The%20first%20images%20were%20produced,soft%20tissues%20like%20the%20brain.
[2] Questions and Answers in MRI https://mriquestions.com/opposite-effects-uarrt1-uarrt2.html
[3] T1-weighted and T2-weighted MRI image synthesis with convolutional generative adversarial networks https://www.ncbi.nlm.nih.gov/pmc/articles/PMC8086713/#:~:text=T1%2Dweighted%20MRI%20enhances%20the,MRI%20image%20analysis%20and%20diagnosis.